XMICRO-SERIAL
Technical Manual
Features:

- Two RS-232 serial ports with 16C550 UARTs
- 115.2 kilobaud maximum transfer speed
- Interrupt-driven PS/2 interface
- Card ID register for system self-configuration
- Fully open-source

Functional Description:

The XMICRO-SERIAL is an XMICRO slave card which provides two high speed RS-232 serial ports and a
PS/2 interface for a keyboard or mouse. The 16C550 UARTs running the RS-232 ports provide a flexible and efficient interface for serial communications. The PS/2 interface uses no programmable or difficult to source ICs and provides full read/write functionality for PS/2 devices. The PS/2 interface also provides error detection, and a data-ready interrupt to minimize CPU overhead.
Tables of Information

Table 1 – Onboard Registers
Address	Function
$X00-$X07	16550 UART 1
$X08-$X0F	16550 UART 2
$X10	PS/2 Data
$X11	Card Status
$XFF	Card ID

Table 2 – Card Configuration
Setting	Function
JP1	Enable UART 1 Interrupt
JP2	Enable UART 2 Interrupt
JP3	Enable PS/2 Interrupt
JP4-7	Shield Ground

Table 4 – Onboard Registers
Address	D7	D6	D5	D4	D3	D2	D1	D0
$X00	N/A			ZP/Stack	A19 Value	A18 Value	A17 Value	A16 Value
$X01	IRQ7 Mask	IRQ6 Mask	IRQ5 Mask	IRQ4 Mask	IRQ3 Mask	IRQ2 Mask	IRQ1 Mask	IRQ0 Mask
$XFF	Card ID

UARTs

Two high performance 16C550 UARTs provide high-speed RS-232 communication through connectors J1 and J2. Table 1 lists the locations of their internal registers. The operation of these UARTs is beyond the scope of this document and may be found in the 16C550 datasheet. A header next to each UART breaks out the two additional user-defined outputs on each UART. These are not used on the card.

75C185 driver/receivers translate signals between TIA-232 compatible voltages and 5V TTL voltages. It is worth noting that these drivers are the main bottleneck that puts the maximum practical communication speed at 115200 baud. Faster drivers and a higher speed crystal could potentially be substituted to provide faster communication, typically at the cost of maximum cable length and driver voltage.

PS/2 Interface

The PS/2 interface was designed from scratch specifically for this card.

Note: If a parity error is detected, software should wait approximately 1ms for the device to finish sending data before reading the data register. This inhibits the device clock for any remaining bytes and allows the shift registers to re-synchronize with the next transmission.

Connector Shield

The connector shields are isolated from the rest of the card to provide flexibility for different system configurations. Ideally this should be isolated and tied to the system chassis, which should then have a good connection to mains-earth. When no other shielding solution is in place, J4-J7 may be shorted to connect the shield net to the card’s ground plane.